## Slide 1: Network Observability : Performance Measurements

## Slide 2: Testbed Setup - Ingress
Receiver
Pktgen1
Observ Agent
Tcnode7
Kernel 5.13
Tcnode6
Kernel 5.4
Questions?
How much % of traffic is successfully monitored by “Observ agent”
What are the overheads?
Observ Logs/Metrics
Eth_protocol, Src_Mac, Dst_Mac, Src_IP, Dest_IP, Src_Port, Dst_port, Protocol =>
Packets, Bytes, FlowStartTime, FlowEndTime
Total Packets = 100 Million
(75B, 1000B packets)
Packet Rate = ~3.7 Mpps
Total threads = 40
(1 UDP Flow per thread)
40 Gbps
1https://github.com/netobserv/ebpf-research/tree/main/PcapPlusPlus/Examples/pktgen
Observ Agent = {pmacct, tcpdump, netobserv-ebpf-agent}

## Slide 3: Results – Monitoring Ingress
Agent | Packets Sent | Packets observed by agent | Monitoring efficacy(%) | Process CPU3(%) 1 Core | Overall CPU4 (%) 80 cores
None | 101,228,092 | 0 | 0 | - | 3.11
Pmacct1 | 101,898,951 | 52,978,667 | 51.99 | 185 | 16.1
Tcpdump | 101,834,300 | 68,618,717 | 67.38 | 45 | 24
Netobserv-ebpf-agent_v1 | 102,109,078 | 9,223,414 | 9 | 195 | 10.07
Netobserv-ebpf-agent_v2 | 100,279,611 | 100,279,611 | 100 | 0.2 | 3.7
Packet Rate (Mpps) = ~3.7 Mpps
1 https://github.com/pmacct/pmacct
*Values averaged over 5 runs
3 pidstat 1 –p <>
4 mpstat 11

## Slide 4: Testbed Setup - Egress
Pktgen
Receiver
Observ Agent
Tcnode7
Kernel 5.13
Tcnode6
Kernel 5.4
Questions?
How much does “Observ agent” slow down throughput of “Pktgen”
How much % of traffic is successfully monitored by “Observ agent”
40 Gbps
Total Packets = 100 M
(75B packets)
Packet Rate = ~4.7 Mpps
Total threads = 40
(1 Flow per thread)
Observ Logs/Metrics
Eth_protocol, Src_Mac, Dst_Mac, Src_IP, Dest_IP, Src_Port, Dst_port, Protocol =>
Packets, Bytes, FlowStartTime, FlowEndTime

## Slide 5: Results – Monitoring Egress
Agent | Packets Sent | Packets observed by agent | Packet Rate (Mpps) | Monitoring efficacy(%) | Process CPU(%) 1 Core | Overall CPU(%) 80 cores
None | 101,537,206 | 0 | 4.7 | - | - | 48.5
Pmacct | 101,636,497 | 65,574,533 | 2.32 | 64.5 | 186 | 51.79
Tcpdump | 100,374,690 | 100,374,690 | 1.65 | 100 | 51 | 51.5
Netobserv-ebpf-agent_v1 | 101,186,109 | 13,037,588 | 2.6 | 12 | 170 | 55.2
Netobserv-ebpf-agent_v2 | 101,300,570 | 101,300,570 | 4.45 | 100 | 0.2 | 48.54
Chart: 
| pmacct | tcpdump | netobserv-ebpf-agent | None
Throughput (Mpps) | 2.32 | 1.65 | 4.45 | 4.7
*Values averaged over 5 runs

## Slide 6: Testbed Setup - TCP
TCP
Receiver
Observ Agent
Tcnode7
Kernel 5.13
Tcnode6
Kernel 5.4
Questions?
How much does “Observ agent” slow down throughput of TCP Flows
40 Gbps
Total Flows = 128
(100B packets)
Duration = 60 sec
Observ Logs/Metrics
Eth_protocol, Src_Mac, Dst_Mac, Src_IP, Dest_IP, Src_Port, Dst_port, Protocol =>
Packets, Bytes, FlowStartTime, FlowEndTime
The TCP Flows are allowed to run for 60 sec, and the final packet throughput (Mpps) is measured
TCP Sender

## Slide 7: Results – Monitoring TCP traffic
Agent | Packets sent (over 60sec period) | Packets observed by agent | Monitoring efficacy (%) | Packet Rate (Mpps) | CPU Extra Overhead (%)
None | 657,309,157 | 0 | 0 | 11.75 | 0
pmacct(print) | 225,467,753 | 71,410,449 | 31.67213411 | 3.5 | 234.2980543
tcpdump | 497,131,749 | 34420750 | 6.923868787 | 7.25 | 51.48792619
netobserv-ebpf-agent_V1 | 220,042,728 | 14,577,508 | 6.624853348 | 3.7 | 220.4064098
netobserv-ebpf-agent_V2 | 611,224,733 | 611,224,733 | 100 | 10.4 | 11.19913195

## Slide 8: Appendix 1: Pmacctd Config
daemonize: true
pcap_interface: ens6f0np0
plugins: print[flows]
!
aggregate[flows]: src_mac, dst_mac, src_host, dst_host, src_port, dst_port, proto
!
print_output_file[flows]: /home/pravein/pmacctd/flows-%Y%m%d_%H%M.txt
print_output[flows]: csv
print_refresh_time[flows]: 100
print_history[flows]: 5m
print_output_file_append[flows]: true
!
print_latest_file[flows]: /home/pravein/pmacctd/flows-latest